PROJECT NUMBER ______________			PROJECT NAME__________________

DATE ___________					PROJECT LOCATION _____________

TECHNICAL SPECIFICATIONS

SECTION 27 16 00 - COMMUNICATIONS DEVICES and ADAPTORS

SECTION 27 16 16 - COMMUNICATIONS ADAPTORS and TRANSCEIVERS

TYPE ER8500U ETHERNET EXTENDER SYSTEM

PART 1 GENERAL

1.01	All equipment to be supplied under this specification shall be new and the current model of a standard product of an OEM of record. An OEM of record shall be defined as a company whose main occupation is the manufacture for sale of the equipment supplied and which:

- Maintains a factory production line for the item submitted.

- Maintains a stock of replacement parts for the item submitted.

- Maintains engineering drawings, specifications, and operating manuals for the items submitted.

- Has published and distributed descriptive literature and equipment specifications on the items of equipment submitted.

1.02	Specifications of equipment as set forth herein are salient and minimum requirements, unless otherwise stated and shall not be construed as limiting the overall quality, quantity or performance characteristics of items furnished.

1.03	System and components shall have been thoroughly tested and proven in actual 	use.

1.04	System and components shall be UL Listed and CE compliant.

1.05	All systems and components shall be provided with the availability of a toll free (U.S. and Canada) technical support number from the manufacturer. The number shall provide technical assistance for either the dealer/installer or the end user at no charge

PART 2 SPECIFICATIONS

2.0.1	The 8 Port Rack Mounted Ethernet and PoE UTP Extender System shall be a NITEK Model ER8500U. The unit along with the ET1500U transmitter(s) shall be capable of providing PoE power and transmitting IP Ethernet network data over up to 8 standard CAT5e or CAT6 cables for distances of up to 600 meters (1,960 feet) on a 10/100 network.

2.0.2	The ER8500U shall have a front panel consisting of numbered LED port indicators from “1” to “8” accompanied by additioanl LED indicators for bandwidth speed rates in increments of “10”, “100”, & “1000” along with port PoE detection, a device power, and trouble status notification alert indicators.

2.0.3	The 8 port Ethernet and PoE UTP Extender System shall have a front panel consisitng of one row of Eight (8) RJ45 input connectors which shall provide a means to connect with IP cameras or other networked devices at 10/100 data rate speeds. Each RJ45 housing shall contain two LED indicators, a white LED to indicate PoE power present and a green LED to indicate Ethernet connectivity. One (1) additional RJ45 connector provides 1 Gigabits of network output connectivity.

PROJECT NUMBER ______________			PROJECT NAME__________________

DATE ___________					PROJECT LOCATION _____________

TECHNICAL SPECIFICATIONS

SECTION 27 16 00 - COMMUNICATIONS DEVICES and ADAPTORS

SECTION 27 16 16 - COMMUNICATIONS ADAPTORS and TRANSCEIVERS

TYPE ER8500U ETHERNET EXTENDER SYSTEM

PART 2 SPECIFICATIONS (Continued)

2.0.4	The 8 RJ45 output connectors shall provide 15.4 watts and 25.5 watts of power to operate 802.3af and or 802.3at compliant network devices. Total power output of the internal PoE Supply shall be 320 watts.

2.0.5	Each of the EPUES’s 8 RJ45 output jacks of the PoE Supply shall automatically detect PoE compliant devices when connected and shall switch on power to the PoE device. When power is present, an integral power indicator LED on the front panel of the unit will be illuminated (see section 2.0.3).

2.0.6	Each of the ER8500U’s 8 RJ45 output jacks shall be protected by an auto-resetting overload device, which shall trip and interrupt the circuit when the rated power has been exceeded. The power shall be automatically reset when the overload is removed.

2.0.7	The Ethernet and PoE UTP Extender System shall operate over a primary line voltage of 115VAC or 230VAC at 50 or 60 Hz with a current level not to exceed 3 amps. The tempatrue rating for the ER8500U shall operate over an ambient temperature range of 0 degrees C – 52 degrees C / 32 - 125 degrees F. Connection to the primary line shall be by means of an IEC320 power connector.

2.0.8	The ER8500U shall have two internal fans to facilitate proper air ciruclation and heat dissapation.

2.0.9	The overall shipping weight of the ER8500U shall be 12Lbs.

2.0.10	The ER8500U shall be constructed of CR steel, painted black and shall fit a standard 19” equipment rack and shall be one rack height. Overall size shall be 1.75” H x 19.0” W x 12.0” D.

2.0.11	The ER8500U shall have a limited lifetime warranty.

# Text boxes

17JUL2013