PROJECT NUMBER ______________			PROJECT NAME__________________

DATE ___________					PROJECT LOCATION _____________

TECHNICAL SPECIFICATIONS

SECTION 28 23 00  - VIDEO SURVEILLANCE

SECTION 28 23 23  - VIDEO SURVEILLANCE SYSTEMS INFRASTRUCTURE

TYPE CAMPVC24 CAMERA VIDEO, POWER, AND PTZ DATA SURGE

PROTECTOR

PART 2 – PRODUCTS

2.1 GENERAL

2.1.1   All equipment to be supplied under this specification shall be new and the current

model of a standard product of an OEM of record. An OEM of record shall be

defined a a company whose main occupation is the manufacture for sale of the

equipment supplied and which:

- Maintains a factory production line for the item submitted.

- Maintains a stock of replacement parts for the item submitted..

- Maintains engineering drawings, specifications, and operating manuals for the items submitted.

- Has published and distributed descriptive literature and equipment specifications on the items of equipment submitted.

    - Specifications of equipment as set forth herein are salient and minimum requirements, unless otherwise stated and shall not be construed as limiting the overall quality, quantity or performance characteristics of items furnished.

    - Systems and components shall have been thoroughly tested and proven in actual use.

    - All systems and components shall be provided with the availability of a toll free (U.S. and Canada) technical support number from the manufacturer. The number shall provide technical assistance for either the dealer/installer or the end user at no charge

2.2  SPECIFICATIONS

    - The camera video, power, and PTZ data surge protector shall be a NITEK Model CAMPVC24 or approved equivalent, and shall be a multi-function surge protector for in-line coaxial video, RS422 twisted pair, the 24 VAC, and 12 VDC camera supply. The CAMPVC24 shall provide protection as stated in paragraph 2.2.2. The CAMPVC24 shall do so via coax BNC connectors and screw input terminals provide multi-stage surge protection to cameras and head-end/control room equipment over RG59 coax cable and twisted pair 24AWG or better wire.

    - The CAMPVC24 shall provide separate protection for all video, power and PTZ data signals into a camera. Camera video signals shall be protected via two (2) Coax BNC connectors labled “Protected” and “Unprotected”. The “Protected” BNC connector shall provide direct protection to the camera video input. Two (2) banks of screw terminals labled “Protected” and “Unprotected” shall provide protection for the camera power and PTZ signlas. The “Protected” terminals provide direct protection for the camera power and PTZ data inputs.

PROJECT NUMBER ______________			PROJECT NAME__________________

DATE ___________					PROJECT LOCATION _____________

TECHNICAL SPECIFICATIONS

SECTION 28 23 00 -  VIDEO SURVEILLANCE

SECTION 28 23 23  - VIDEO SURVEILLANCE SYSTEMS INFRASTRUCTURE

TYPE CAMPVC24 CAMERA VIDEO, POWER, AND PTZ DATA SURGE

PROTECTOR

PART 2 – PRODUCTS (Continued)

    - The NITEK CAMPVC24 shall be capable of protecting all camera signal inputs from harmful surges, spikes, and transients. The CAMPVC24 shall have a clamping voltage of 2.8 up to 100,000 volts.

    - The CAMPVC24 shall be of the multi-stage clamping design.

    - The CAMPVC24 shall not require power to operate as specified.

    - The CAMPVC24 shall have a heavy single point cooper ground lug to accommodate proper earth to grounding procedures.

    - The CAMPVC24 camera signal inputs shall be indicated by “Protected” and signal outputs shall be indicated by the “Unprotected” identifier.

    - The CAMPVC24 shall be able to be installed at the exterior camera site or at the head-end/control room location.

    - The CAMPVC24 shall operate within specifications without causing interference or interfering with base band video, communication, data and/or low-voltage signals operating over coax, twisted pair, or non-stranded power cables as specified in paragraph 2.2.1.

2.2.10	The CAMPVC24 shall be covered by a Limited Lifetime Warranty.

PROJECT NUMBER ______________			PROJECT NAME__________________

DATE ___________					PROJECT LOCATION _____________

TECHNICAL SPECIFICATIONS

SECTION 28 23 00 -  VIDEO SURVEILLANCE

SECTION 28 23 23  - VIDEO SURVEILLANCE SYSTEMS INFRASTRUCTURE

TYPE CAMPVC24 CAMERA VIDEO, POWER, AND PTZ DATA SURGE

PROTECTOR

2.3  PERFORMANCE SPECIFICATIONS

    - The CAMPVC24 shall meet or exceed the following performance specifications:

- The surge protector device shall be capable of passing through a color video signal of NTSC standard 525 lines or PAL standard 625 lines.

- Video Format compatibility: RS170, NTSC, PAL, SECAM, CCIR (Color or Monochrome).

- Connection Methods: Video – Female BNC Connectors, Power – Screw Terminlas, PTZ Data – Screw Terminals

- Clamping Voltage: Video – 2.8V, Power – 33Vrms, PTZ data control – 4.7V.

- Transient Protection: IEC61000-4-4 (EFT) 40A (5/50ns) IEC61000-4-5 (Lightning) 24A (8/20μs)

- Voltage requirements: No Power Supply is required.

- Power consumption: None

- Video Insertion Loss: <0.2dB

- Impedance: 50 or 75 Ohms

- Frequency: DC to 10 MHz

- Shipping Weight: 1 lb / 0.453 kg

- The dimension are 1.7” H x 4.3” W x 2.5” D.

- Temperature of -40°C to +85°C/ -40°F to 185°F

17JUL2013