UNSHIELDED TWISTED PAIR ACTIVE VIDEO SYSTEM – TYPE EX560

TECHNICAL SPECIFICATIONS					    SECURITY SYSTEM

DIVISION 16 – ELECTRICAL

SECTION 16 _ _ _  - CLOSED CIRCUIT TELEVISION (CCTV) SYSTEM

PART 2 – PRODUCTS

2.1 GENERAL

2.1.1   All equipment to be supplied under this specification shall be new and the  current

model of a standard product of an OEM of record. An OEM of record shall be

defined a a company whose main occupation is the manufacture for sale of the

equipment supplied and which:

- Maintains a factory production line for the item submitted.

- Maintains a stock of replacement parts for the item submitted..

- Maintains engineering drawings, specifications, and operating manuals for the items submitted.

- Has published and distributed descriptive literature and equipment specifications on the items of equipment submitted.

    - Specifications of equipment as set forth herein are salient and minimum requirements, unless otherwise stated and shall not be construed as limiting the overall quality, quantity or performance characteristics of items furnished.

    - Systems and components shall have been thoroughly tested and proven in actual use.

    - All systems and components shall be provided with the availability of a toll free (U.S. and Canada) technical support number from the manufacturer. The number shall provide technical assistance for either the dealer/installer or the end user at no charge

2.2  SPECIFICATIONS

2.2.1     The Twisted pair active video system, shall be a NITEK Model EX560 or

approved equivalent, and shall be capable of receiving baseband type

monochrome or color video signals over unshielded twisted pair (UTP) telephone

cables, Category 3 or better, 24 gage or heavier up to a maximum cable length of

6,000 feet (1800 meters).

    - The EX560 System shall consist of a NITEK Model TR560 active receiver unit or approved equivalent and a NITEK Model TT560 active transmitter unit or approved equivalent.

    - Receiving video signals, as described in paragraph 2.2.1 shall mean that the active video system shall be capable of delivering a monochrome or color video signal of 500 lines at the maximum specified distance.

    - The active receiver and active transmitter units shall be provided with  power supplies, which shall have provisions to plug directly into a 120 VAC wall outlet and shall provide an  output voltage within the specifications of paragraph 2.3E. Output voltage for each shall be provided over two appropriate gauge wires (2 foot minimum length) for connection to the receiver and the transmitter power input terminals.

UNSHIELDED TWISTED PAIR ACTIVE VIDEO RECEIVER – TYPE EX560

TECHNICAL SPECIFICATIONS					    SECURITY SYSTEM

DIVISION 16 – ELECTRICAL

SECTION 16 _ _ _  - CLOSED CIRCUIT TELEVISION (CCTV) SYSTEM

PART 2 – PRODUCTS (continued)

  - SPECIFICATIONS (continued)

    - The active receiver shall provide frequency equalization by means of eight dual

in-line (DIP) switches. The switches shall provide compensation for varying cable lengths from 500 to 6,000 feet.

2.2.6	The active transmitter shall provide signal amplification and frequency equalization by means of four dual in-line (DIP) switches. The effect of the switches in both the transmitter and receiver units shall be to equalize and to amplify the video signal thereby providing loss compensation for video as cable length is increased.

    - The active system shall be capable of equalizing a color video signal of NTSC

standard 525 lines or PAL standard 625 lines and shall deliver a baseband video

signal capable of driving a 75 ohm impedance load.

.

2.2.8	The transmitter and receiver units shall have built-in transient protection.

2.2.9	Video connection to the active transmitter and receiver units shall be by means

of a BNC type female connector. A five screw terminal block shall provide connection to the UTP cable (2), 12 VDC power supply (2) and earth ground (1).

2.2.10	The active system shall operate within specifications without causing

interference or interfering with any other base band video, communication, data

and/or other low-voltage signals operating in multi-twisted pair UTP cables as

specified in paragraph 2.2.1.

2.2.11  The active system shall be covered by a Limited Two Year Warranty.

2.3  PERFORMANCE SPECIFICATIONS

    - The active system shall meet or exceed the following performance specifications:

- With a symmetrical and balanced composite input from the transmitter unit and using cables as specified in paragraph 2.2.2, at a cable length of 6,000 feet, the output from the receiver unit shall be a 1 Vpp composite video signal into 75 ohms.

- The  receiver unit shall be capable of receiving RS170, NTSC, PAL, SECAM and CCIR video formats (color or monochrome).

UNSHIELDED TWISTED PAIR ACTIVE VIDEO RECEIVER – TYPE EX560

TECHNICAL SPECIFICATIONS					    SECURITY SYSTEM

DIVISION 16 – ELECTRICAL

SECTION 16 _ _ _  - CLOSED CIRCUIT TELEVISION (CCTV) SYSTEM

PART 2 – PRODUCTS (continued)

  - PERFORMANCE SPECIFICATIONS (continued)

- Operating frequency range: DC to 10 MHz.

- Common mode rejection to be > 70 dB.

- Voltage requirements: 12 to 24 VAC or DC (Power Supplies provided).

- Size: Both transmitter and receiver units: Enclosures to be Black Cycolac ABS Flame Retardent Thermoplastic with a maximum size of 1.25”h x 1.5”w x .75”d (w = 2.25” including BNC connector).

H .Temperature: System must operate in an ambient temperature of –40

Degrees C to +85 degrees C, 0 to 98% non-condensing.